PAKISTAN STANDARDS SPECIFICATION

FOR

POTASSIUM SULPHATE (SULPHATE OF POTASH)

FERTILIZER GRADE, (2nd Revision)

Table-1

REQUIREMENTS FOR POTASSIUM SULPHATE (FERTILIZER GRADE)

| S. No | Characteristics | Requirements | Method of tests |
| --- | --- | --- | --- |
| 01 | Physical condition | Free flowing granular or crystalline | Visual inspection |
| 02 | Moisture% by weight, max | 1.0 | Appendix – B |
| 03 | Potassium content( as K2O % by weight) min. | 50.0 | Appendix – C |
| 04 | Total chlorides (as Cl), % by weight), (on dry basis) max. | 2.5 | Appendix – C C- 5 |
| 05. | Particle size | 90% between 0.25 to 3mm. | Appendix – D |
| 06 | Sodium (as NaCl) % by weight, max | 2 | Appendix – E |
| 07 | Sulfur % by weight, min. | 17.5 | Appendix – F |

TABLE – III

CRITERION FOR CONFORMITY

| S.# | Characteristic | Test Results 1.2…. n | Mean | Range | Criterion for Conformity |
| --- | --- | --- | --- | --- | --- |
| i. | ii. | iii | iv | v | vi |
| 1 | Total potash, percent by weight | -- | X | R | x─0.6 R≥ the value specified in Table (1) |