Only for Research Purpose

Truck and bus tyres and rims (metric series) —

Part 1:

Tyres

Not For Sale- PSQCA (c)

Pneumatiques et jantes (séries millimétriques) pour camions et autobus — Partie 1: Pneumatiques

Reference number ISO 4209-1:2001(E)

Only for Research Purpose

| Code | Nominal rim diameter Dr mm |
| --- | --- |
| 5° tapered rims | 15° tapered (drop-centre) rims |  |
| 10 | — | 254 |
| 12 | — | 305 |
| 13 | — | 330 |
| 14 | — | 356 |
| 15 | — | 381 |
| 16 | — | 406 |
| 17 | — | 432 |
| — | 17.5 | 445 |
| 18 | — | 457 |
| — | 19.5 | 495 |
| 20 | — | 508 |
| — | 20.5 | 521 |
| 22 | — | 559 |
| — | 22.5 | 572 |
| 24 | — | 610 |
| — | 24.5 | 622 |

| Code | Rim width mm |
| --- | --- |
| 5° tapered rims | 15° tapered (drop-centre) rims |  |
| 3.00 | — | 76 |
| 3.50 | — | 89 |
| 4.00 | — | 101,5 |
| 4.50 | — | 114,5 |
| 5.00 | — | 127 |
| — | 5.25 | 133,5 |
| 5.50 | — | 139,5 |
| 6.00 | 6.00 | 152,5 |
| 6.50 | — | 165 |
| — | 6.75 | 171,5 |
| 7.00 | — | 178 |
| 7.50 | 7.50 | 190,5 |
| 8.00 | — | 203 |
| — | 8.25 | 209,5 |
| 8.50 | — | 216 |
| 9.00 | 9.00 | 228,5 |
| 9.50 | — | 241,5 |
| — | 9.75 | 247,5 |
| 10.00 | — | 254 |
| 10.50 | 10.50 | 266,5 |
| 11.00 | — | 279.5 |
| — | 11.75 | 298,5 |
| 12.00 | — | 305 |
| — | 12.25 | 311 |
| 13.00 | 13.00 | 330 |
| 14.00 | 14.00 | 355,5 |
| 15.00 | 15.00 | 381 |
| — | 16.00 | 406,5 |
| — | 17.00 | 432 |
| — | 18.00 | 457 |

Not For Sale- PSQCA (c)

Table 1 — Nominal rim diameter codes	Table 2 — Rim width codes

Table 3 — Coefficients K2, b, a for calculation of tyre dimensions

| Structure | Tyre construction code | Coefficients |
| --- | --- | --- |
|  |  | K2 | NOTE b a | a |
| Bias-belted | B | 0,4 | 1,07 | 1,08 |
| Diagonal | D | 0,4 | 1,07 | 1,08 |
| Radial | R | 0,4 | 1,04 | 1,05 |
| a For special tread tyres (see 4.4.3): Bias-belted: b = 1,09 Diagonal: b = 1,09 Radial: b = 1,06 |
| NOTE Other factors may be established for new tyre concepts (constructions). |

Not For Sale- PSQCA (c)

Table 4 — Coefficients K1, K3, K4 for calculation of tyre dimensions

| Tyre construction code | Type of rim | Nominal aspect ratio H/S | Theoretical rim/section ratio K1 | Minimum dual spacing K3 | Measuring rim/section ratio K4 |
| --- | --- | --- | --- | --- | --- |
| B, D, R | 5° tapered | 100 to 75 | 0,70 | 1,15 | 0,70 |
|  |  | 70 and 65 | 0,70 | 1,15 | 0,75 |
|  |  | 60 | 0,70 | 1,15 | 0,75 |
|  |  | 55 | 0,70 | 1,15 | 0,80 |
|  |  | 50 a | 0,70 | 1,15 | 0,80 |
|  | 15° tapered (drop-centre) | 90 to 65 | 0,75 | 1,125 | 0,75 |
|  |  | 60 | 0,80 | 1,125 | 0,80 |
|  |  | 55 | 0,80 | 1,125 | 0,80 |
|  |  | 50 | 0,80 | — | 0,80 |
|  |  | 45 a | 0,85 | — | 0,85 |
| a For H/S lower than 50 or 45 respectively, further coefficients will be established. |
| NOTE Other factors may be established for new tyre concepts (constructions). |

Only for Research Purpose

Table 5 — Coefficients for calculation of rim widths

| Type of rim | Nominal aspect ratio H/S | Coefficients for calculation of approved rim width a CR |
| --- | --- | --- |
|  |  | min. | max. |
| 5° tapered | 100 to 75 | 0,65 | 0,80 |
|  | 70 | 0,675 | 0,80 |
|  | 65 | 0,70 | 0,80 |
|  | 60 | 0,725 | 0,825 |
|  | 55 | 0,75 | 0,825 |
|  | 50 b | 0,75 | 0,825 |
| 15° tapered | 90 to 70 | 0,70 | 0,80 |
|  | 60 and 65 | 0,75 | 0,825 |
|  | 55 | 0,775 | 0,825 |
|  | 50 | 0,80 | 0,85 |
|  | 45 b | 0,80 | 0,85 |
| Other coefficients may be specified in relation to special services by agreement among tyre, rim, wheel and motor vehicle manufacturers. For H/S lower than 50 and 45 respectively, further coefficients will be established. |

Not For Sale- PSQCA (c)

Only for Research Purpose

Not For Sale- PSQCA (c)

Table 6 — Correlation between load index and tyre load-carrying capacity (TLCC)

| Load Index (LI) | TLCC kg | Load Index (LI) | TLCC kg | Load Index (LI) | TLCC kg | Load Index (LI) | TLCC kg | Load Index (LI) | TLCC kg | Load Index (LI) | TLCC kg | Load Index (LI) | TLCC kg |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 46 | 40 | 140 | 80 | 450 | 120 | 1 400 | 160 | 4 500 | 200 | 14 000 | 240 | 45 000 |
| 1 | 46,2 | 41 | 145 | 81 | 462 | 121 | 1 450 | 161 | 4 625 | 201 | 14 500 | 241 | 46 250 |
| 2 | 47,5 | 42 | 150 | 82 | 475 | 122 | 1 500 | 162 | 4 750 | 202 | 15 000 | 242 | 47 750 |
| 3 | 48,7 | 43 | 155 | 83 | 487 | 123 | 1 550 | 163 | 4 875 | 203 | 15 500 | 243 | 48 750 |
| 4 | 50 | 44 | 160 | 84 | 500 | 124 | 1 600 | 164 | 5 000 | 204 | 16 000 | 244 | 50 000 |
| 5 | 51,5 | 45 | 165 | 85 | 515 | 125 | 1 650 | 165 | 5 150 | 205 | 16 500 | 245 | 51 500 |
| 6 | 53 | 46 | 170 | 86 | 530 | 126 | 1 700 | 166 | 5 300 | 206 | 17 000 | 246 | 53 000 |
| 7 | 54,5 | 47 | 175 | 87 | 545 | 127 | 1 750 | 167 | 5 450 | 207 | 17 500 | 247 | 54 500 |
| 8 | 56 | 48 | 180 | 88 | 560 | 128 | 1 800 | 168 | 5 600 | 208 | 18 000 | 248 | 56 000 |
| 9 | 58 | 49 | 185 | 89 | 580 | 129 | 1 850 | 169 | 5 800 | 209 | 18 500 | 249 | 58 000 |
| 10 | 60 | 50 | 190 | 90 | 600 | 130 | 1 900 | 170 | 6 000 | 210 | 19 000 | 250 | 60 000 |
| 11 | 61,5 | 51 | 195 | 91 | 615 | 131 | 1 950 | 171 | 6 150 | 211 | 19 500 | 251 | 61 500 |
| 12 | 63 | 52 | 200 | 92 | 630 | 132 | 2 000 | 172 | 6 300 | 212 | 20 000 | 252 | 63 000 |
| 13 | 65 | 53 | 206 | 93 | 650 | 133 | 2 060 | 173 | 6 500 | 213 | 20 600 | 253 | 65 000 |
| 14 | 67 | 54 | 212 | 94 | 670 | 134 | 2 120 | 174 | 6 700 | 214 | 21 200 | 254 | 67 000 |
| 15 | 69 | 55 | 218 | 95 | 690 | 135 | 2 180 | 175 | 6 900 | 215 | 21 800 | 255 | 69 000 |
| 16 | 71 | 56 | 224 | 96 | 710 | 136 | 2 240 | 176 | 7 100 | 216 | 22 400 | 256 | 71 000 |
| 17 | 73 | 57 | 230 | 97 | 730 | 137 | 2 300 | 177 | 7 300 | 217 | 23 000 | 257 | 73 000 |
| 18 | 75 | 58 | 236 | 98 | 750 | 138 | 2 360 | 178 | 7 500 | 218 | 23 600 | 258 | 75 000 |
| 19 | 77,5 | 59 | 243 | 99 | 775 | 139 | 2 430 | 179 | 7 750 | 219 | 24 300 | 259 | 77 500 |
| 20 | 80 | 60 | 250 | 100 | 800 | 140 | 2 500 | 180 | 8 000 | 220 | 25 000 | 260 | 80 000 |
| 21 | 82,5 | 61 | 257 | 101 | 825 | 141 | 2 575 | 181 | 8 250 | 221 | 25 750 | 261 | 82 500 |
| 22 | 85 | 62 | 265 | 102 | 850 | 142 | 2 650 | 182 | 8 500 | 222 | 26 500 | 262 | 85 000 |
| 23 | 87,5 | 63 | 272 | 103 | 875 | 143 | 2 725 | 183 | 8 750 | 223 | 27 250 | 263 | 87 500 |
| 24 | 90 | 64 | 280 | 104 | 900 | 144 | 2 800 | 184 | 9 000 | 224 | 28 000 | 264 | 90 000 |
| 25 | 92,5 | 65 | 290 | 105 | 925 | 145 | 2 900 | 185 | 9 250 | 225 | 29 000 | 265 | 92 500 |
| 26 | 95 | 66 | 300 | 106 | 950 | 146 | 3 000 | 186 | 9 500 | 226 | 30 000 | 266 | 95 000 |
| 27 | 97,5 | 67 | 307 | 107 | 975 | 147 | 3 075 | 187 | 9 750 | 227 | 30 750 | 267 | 97 500 |
| 28 | 100 | 68 | 315 | 108 | 1 000 | 148 | 3 150 | 188 | 10 000 | 228 | 31 500 | 268 | 100 000 |
| 29 | 103 | 69 | 325 | 109 | 1 030 | 149 | 3 250 | 189 | 10 300 | 229 | 32 500 | 269 | 103 000 |
| 30 | 106 | 70 | 335 | 110 | 1 060 | 150 | 3 350 | 190 | 10 600 | 230 | 33 500 | 270 | 106 000 |
| 31 | 109 | 71 | 345 | 111 | 1 090 | 151 | 3 450 | 191 | 10 900 | 231 | 34 500 | 271 | 109 000 |
| 32 | 112 | 72 | 355 | 112 | 1 120 | 152 | 3 550 | 192 | 11 200 | 232 | 35 500 | 272 | 112 000 |
| 33 | 115 | 73 | 365 | 113 | 1 150 | 153 | 3 650 | 193 | 11 500 | 233 | 36 500 | 273 | 115 000 |
| 34 | 118 | 74 | 375 | 114 | 1 180 | 154 | 3 750 | 194 | 11 800 | 234 | 37 500 | 274 | 118 000 |
| 35 | 121 | 75 | 387 | 115 | 1 215 | 155 | 3 875 | 195 | 12 150 | 235 | 38 750 | 275 | 121 000 |
| 36 | 125 | 76 | 400 | 116 | 1 250 | 156 | 4 000 | 196 | 12 500 | 236 | 40 000 | 276 | 125 000 |
| 37 | 128 | 77 | 412 | 117 | 1 285 | 157 | 4 125 | 197 | 12 850 | 237 | 41 250 | 277 | 128 500 |
| 38 | 132 | 78 | 425 | 118 | 1 320 | 158 | 4 250 | 198 | 13 200 | 238 | 42 500 | 278 | 132 000 |
| 39 | 136 | 79 | 437 | 119 | 1 360 | 159 | 4 375 | 199 | 13 600 | 239 | 43 750 | 279 | 136 000 |

Only for Research Purpose

Table 7 — Correlation between speed symbol and speed category

| Speed symbol | Speed category km/h |
| --- | --- |
| B | 50 |
| C | 60 |
| D | 65 |
| E | 70 |
| F | 80 |
| G | 90 |
| J | 100 |
| K | 110 |
| L | 120 |
| M | 130 |
| N | 140 |
| P | 150 |
| Q | 160 |
| R | 170 |
| S | 180 |
| T | 190 |
| H | 210 |

Not For Sale- PSQCA (c)

Table 8 — Load-carrying capacities at various speeds — Tyres with load index (single) u 121 and speed symbol J and above

| Speed km/h | Load, %, for speed symbol |
| --- | --- |
|  | J | K | L | M | N | P | Q | R | S | T | H |
| Static | 250 | 250 | 210 | See Column L | See column L | See column L | See column L | See column L | See column L | See column L | See column L |
| 10 | 180 | 180 | 175 |  |  |  |  |  |  |  |  |
| 15 | 165 | 165 | 160 |  |  |  |  |  |  |  |  |
| 30 | 125 | 125 | 135 |  |  |  |  |  |  |  |  |
| 50 | 112 | 112 | 120 |  |  |  |  |  |  |  |  |
| 70 | 107 | 107 | 112,5 |  |  |  |  |  |  |  |  |
| 85 | 103 | 103 | 108,5 |  |  |  |  |  |  |  |  |
| 100 | 100 | 100 | 105 |  |  |  |  |  |  |  |  |
| 110 | 96 | 100 | 102,5 |  |  |  |  |  |  |  |  |
| 120 | 88 | 93 | 100 |  |  |  |  |  |  |  |  |
| 130 | — | — | 95 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 |
| 140 |  |  | 90 | 95 |  |  |  |  |  |  |  |
| 150 |  |  | — | — | — |  |  |  |  |  |  |
| 160 |  |  |  |  |  | — |  |  |  |  |  |
| 170 |  |  |  |  |  |  | — |  |  |  |  |
| 180 |  |  |  |  |  |  |  | — |  |  |  |
| 190 |  |  |  |  |  |  |  |  | — |  |  |
| 210 |  |  |  |  |  |  |  |  |  | — |  |
| NOTE 1 The inflation pressure shall be increased for load adjustments above 125 % or for speeds above 160 km/h in consultation with the tyre manufacturer. NOTE 2 Load adjustments are valid for use on improved surface only. NOTE 3 Consult rim and wheel manufacturers for confirmation of the strength of the rim/wheel for the intended service. NOTE 4 For 70 km/h and above "speed" means the speed capability of the vehicle (maximum speed under fully laden conditions). For 65 km/h and below, "speed" means the operating speed of the vehicle. |

Not For Sale- PSQCA (c)

Table 9 — Load-carrying capacities at various speeds — Tyres with load index (single) W 122, speed symbols F to M

| Speed km/h | Load, %, for speed symbol |
| --- | --- |
|  | F | G | J | K | L | M |
| Static | 250 | See column F |
| 10 | 180 |  |
| 15 | 165 |  |
| 30 | 125 |  |
| 50 | 112 |  |
| 65 | 107,5 | 108,5 | 108,5 | See column J |
| 80 | 100 | 104 | 104 |  |
| 90 | 94 | 100 | 102 |  |
| 100 | 85 | 95 | 100 |  |
| 110 | — | 87 | 96 | 100 | 100 | 100 |
| 120 |  | — | 88 | 93 | 100 | 100 |
| 130 |  |  | — | — | — | 100 |
| NOTE 1 The inflation pressure shall be increased for load adjustments above 125 % in consultation with the tyre manufacturer. NOTE 2 Load adjustments are valid for use on improved surface only. NOTE 3 Consult rim and wheel manufacturers for confirmation of the strength of the rim/wheel for the intended service. NOTE 4 For 70 km/h and above "speed" means the speed capability of the vehicle (maximum speed under fully laden conditions). For 65 km/h and below, "speed" means the operating speed of the vehicle. |

Only for Research Purpose

Annex A

(informative)

Guideline values for metric series, 5° rims

These values will serve as a guideline for the design of tyre dimensions, metric series, mounted on 5° tapered drop-centre rims (code-designated) with nominal rim diameters up to code 16 inclusive. For tyres mounted on 15° tapered drop-centre rims (code-designated), see annex B. For tyres mounted on different types of rims (millimetre- designated), other annexes will be established.

Not For Sale- PSQCA (c)

Table A.1 — Dimensional guidelines for metric “100” to “75” series tyres on 5° tapered rims

| Nominal section width SN mm | Measuring rim width code Rm | Tyre design dimensions, mm |
| --- | --- | --- |
|  |  | Design section width S | Design section height a, H | Approved rim width codes |
|  |  |  | Nominal aspect ratios, H/S |  |
|  |  |  | 100 | 95 | 90 | 85 | 80 | 75 | min. | max. |
| 125 | 3.50 | 126 | 125 | 119 | 113 | 106 | 100 | 94 | 3 | 4 |
| 135 | 3.50 | 133 | 135 | 128 | 122 | 115 | 108 | 101 | 3.5 | 4.5 |
| 145 | 4.00 | 145 | 145 | 138 | 131 | 123 | 116 | 109 | 3.5 | 4.5 |
| 155 | 4.50 | 157 | 155 | 147 | 140 | 132 | 124 | 116 | 4 | 5 |
| 165 | 4.50 | 165 | 165 | 157 | 149 | 140 | 132 | 124 | 4 | 5 |
| 175 | 5.00 | 177 | 175 | 166 | 158 | 149 | 140 | 131 | 4.5 | 5.5 |
| 185 | 5.00 | 184 | 185 | 176 | 167 | 157 | 148 | 139 | 4.5 | 6 |
| 195 | 5.50 | 196 | 195 | 185 | 176 | 166 | 156 | 146 | 5 | 6 |
| 205 | 5.50 | 203 | 205 | 195 | 185 | 174 | 164 | 154 | 5 | 6.5 |
| 215 | 6.00 | 216 | 215 | 204 | 194 | 183 | 172 | 161 | 5.5 | 7 |
| 225 | 6.00 | 223 | 225 | 214 | 203 | 191 | 180 | 169 | 6 | 7 |
| 235 | 6.50 | 235 | 235 | 223 | 212 | 200 | 188 | 176 | 6 | 7.5 |
| 245 | 7.00 | 248 | 245 | 233 | 221 | 208 | 196 | 184 | 6.5 | 7.5 |
| 255 | 7.00 | 255 | 255 | 242 | 230 | 217 | 204 | 191 | 6.5 | 8 |
| 265 | 7.50 | 2.67 | 265 | 252 | 239 | 225 | 212 | 199 | 7 | 8.5 |
| 275 | 7.50 | 274 | 275 | 261 | 248 | 234 | 220 | 206 | 7 | 8.5 |
| 285 | 8.00 | 286 | 285 | 271 | 257 | 242 | 228 | 214 | 7.5 | 9 |
| 295 | 8.00 | 294 | 295 | 280 | 266 | 251 | 236 | 221 | 7.5 | 9.5 |
| 305 | 8.50 | 306 | 305 | 290 | 275 | 259 | 244 | 229 | 8 | 9.5 |
| 315 | 8.50 | 313 | 315 | 299 | 284 | 268 | 252 | 236 | 8 | 10 |
| 325 | 9.00 | 325 | 325 | 309 | 293 | 276 | 260 | 244 | 8.5 | 10 |
| 335 | 9.00 | 333 | 335 | 318 | 302 | 285 | 268 | 251 | 8.5 | 10.5 |
| 345 | 9.50 | 345 | 345 | 328 | 311 | 293 | 276 | 259 | 9 | 11 |
| 355 | 10.00 | 357 | 355 | 337 | 320 | 302 | 284 | 266 | 9 | 11 |
| 365 | 10.00 | 364 | 365 | 347 | 329 | 310 | 292 | 274 | 9.5 | 11.5 |
| a The figures are based on normal tread pattern tyres. |

Not For Sale- PSQCA (c)

Table A.2 — Dimensional guidelines for metric “70”, “65” and “60” series tyres on 5° tapered rims

| Nominal section width SN mm | Theoretic. rim width Rth K1 = 0,70 | Measuring rim width code Rm K4 = 0,75 | Design section width S mm | Design section height a, H mm | Approved rim width codes |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | min. | max. |
|  |  |  |  | Nominal aspect ratios, H/S | Nominal aspect ratios, H/S | Nominal aspect ratios, H/S |
|  |  |  |  | 70 | 65 | 60 | 70 | 65 | 60 | 70 and 65 | 60 |
| 165 | 4,55 | 5,0 | 170 | 116 | 107 | 99 | 4.5 | 4.5 | 4.5 | 5 | 5.5 |
| 175 | 4,82 | 5,0 | 177 | 123 | 114 | 105 | 4.5 | 5 | 5 | 5.5 | 5.5 |
| 185 | 5,10 | 5,5 | 189 | 130 | 120 | 111 | 5 | 5 | 5.5 | 6 | 6 |
| 195 | 5,37 | 6,0 | 201 | 137 | 127 | 117 | 5 | 5.5 | 5.5 | 6 | 6.5 |
| 205 | 5,65 | 6,0 | 209 | 144 | 133 | 123 | 5.5 | 5.5 | 6 | 6.5 | 6.5 |
| 215 | 5,93 | 6,5 | 221 | 151 | 140 | 129 | 5.5 | 6 | 6 | 7 | 7 |
| 225 | 6,20 | 6,5 | 228 | 158 | 146 | 135 | 6 | 6 | 6.5 | 7 | 7.5 |
| 235 | 6,48 | 7,0 | 240 | 165 | 153 | 141 | 6 | 6.5 | 6.5 | 7.5 | 7.5 |
| 245 | 6,75 | 7,0 | 248 | 172 | 159 | 147 | 6.5 | 7 | 7 | 7.5 | 8 |
| 255 | 7,03 | 7,5 | 260 | 179 | 166 | 153 | 7 | 7 | 7.5 | 8 | 8.5 |
| 265 | 7,30 | 8,0 | 272 | 186 | 172 | 159 | 7 | 7.5 | 7.5 | 8.5 | 8.5 |
| 275 | 7,58 | 8,0 | 279 | 193 | 179 | 165 | 7.5 | 7.5 | 8 | 8.5 | 9 |
| 285 | 7,85 | 8,5 | 292 | 200 | 185 | 171 | 7.5 | 8 | 8 | 9 | 9.5 |
| 295 | 8,13 | 8,5 | 299 | 207 | 192 | 177 | 8 | 8 | 8.5 | 9.5 | 9.5 |
| 305 | 8,41 | 9,0 | 311 | 214 | 198 | 183 | 8 | 8.5 | 8.5 | 9.5 | 10 |
| 315 | 8,68 | 9,5 | 323 | 221 | 205 | 189 | 8.5 | 8.5 | 9 | 10 | 10 |
| 325 | 8,96 | 9,5 | 331 | 228 | 211 | 195 | 8.5 | 9 | 9.5 | 10 | 10.5 |
| 335 | 9,23 | 10,0 | 343 | 235 | 218 | 201 | 9 | 9 | 9.5 | 10.5 | 11 |
| 345 | 9,51 | 10,0 | 350 | 242 | 224 | 207 | 9 | 9.5 | 10 | 11 | 11 |
| 355 | 9,78 | 10,5 | 362 | 249 | 231 | 213 | 9.5 | 10 | 10 | 11 | 11.5 |
| 365 | 10,06 | 11,0 | 375 | 256 | 237 | 219 | 9.5 | 10 | 10.5 | 11.5 | 12 |
| a The figures are based on normal tread pattern tyres. |

Not For Sale- PSQCA (c)

Table A.3 — Dimensional guidelines for metric series “55” and “50” series tyres on 5° tapered rims

| Nominal section width SN mm | Theoretical rim width Rth K1 = 0,70 | Measuring rim width code Rm K4 = 0,80 | Design section width S mm | Design section height a, H mm | Approved rim width codes |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Nominal aspect ratios, H/S |  |
|  |  |  |  | 55 | 50 | min. | max. |
| 165 | 4,55 | 5,0 | 170 | 91 | 83 | 5 | 5.5 |
| 175 | 4,82 | 5,5 | 182 | 96 | 88 | 5 | 5.5 |
| 185 | 5,10 | 6,0 | 194 | 102 | 93 | 5.5 | 6 |
| 195 | 5,37 | 6,0 | 201 | 107 | 98 | 6 | 6.5 |
| 205 | 5,65 | 6,5 | 214 | 113 | 103 | 6 | 6.5 |
| 215 | 5,93 | 7,0 | 226 | 118 | 108 | 6.5 | 7 |
| 225 | 6,20 | 7,0 | 233 | 124 | 113 | 6.5 | 7.5 |
| 235 | 6,48 | 7,5 | 245 | 129 | 118 | 7 | 7.5 |
| 245 | 6,75 | 7,5 | 253 | 135 | 123 | 7 | 8 |
| 255 | 7,03 | 8,0 | 265 | 140 | 128 | 7.5 | 8.5 |
| 265 | 7,30 | 8,5 | 277 | 146 | 133 | 8 | 8.5 |
| 275 | 7,58 | 8,5 | 284 | 151 | 138 | 8 | 9 |
| 285 | 7,85 | 9,0 | 297 | 157 | 143 | 8.5 | 9.5 |
| 295 | 8,13 | 9,5 | 309 | 162 | 148 | 8.5 | 9.5 |
| 305 | 8,41 | 9,5 | 316 | 168 | 153 | 9 | 10 |
| 315 | 8,68 | 10,0 | 328 | 173 | 158 | 9.5 | 10 |
| 325 | 8,96 | 10,0 | 336 | 179 | 163 | 9.5 | 10.5 |
| 335 | 9,23 | 10,5 | 348 | 184 | 168 | 10 | 11 |
| 345 | 9,51 | 11,0 | 360 | 190 | 173 | 10 | 11 |
| 355 | 9,78 | 11,0 | 367 | 195 | 178 | 10.5 | 11.5 |
| 365 | 10,06 | 11,5 | 380 | 201 | 183 | 11 | 12 |
| a The figures are based on normal tread pattern tyres. |

Annex B

(informative)

Guideline values for metric series, 15° rims

These values will serve as a guideline for the design of tyre dimensions, metric series, mounted on 15° tapered drop-centre rims (code-designated). For tyres mounted on 5° tapered drop-centre rims (code-designated), see annex A. For tyres mounted on different types of rims (millimetre-designated), other annexes will be established.

Not For Sale- PSQCA (c)

Table B.1 — Guideline values for metric “90” to “65” series tyres on 15° tapered drop-centre rims

| Nominal section width ab SN mm | Measuring rim width code Rm | Design section width S mm | Design section height c, H mm | Approved rim width codes d |
| --- | --- | --- | --- | --- |
|  |  |  |  | Nominal aspect ratios, H/S 90 to 70 | Nominal aspect ratio, H/S 65 |
|  |  |  | Nominal aspect ratios, H/S |  |  |
|  |  |  | 90 | 85 | 80 | 75 | 70 | 65 | min. | max. | min. | max. |
| 175 | 5.25 | 176 | 158 | 149 | 140 | 131 | 123 | 114 | 5.25 | 5.25 | 5.25 | 6.00 |
| 185 | 5.25 | 183 | 167 | 157 | 148 | 139 | 130 | 120 | 5.25 | 6.00 | 5.25 | 6.00 |
| 195 | 6.00 | 197 | 176 | 166 | 156 | 146 | 137 | 127 | 5.25 | 6.00 | 6.00 | 6.00 |
| 205 | 6.00 | 204 | 185 | 174 | 164 | 154 | 144 | 133 | 6.00 | 6.75 | 6.00 | 6.75 |
| 215 | 6.00 | 211 | 194 | 183 | 172 | 161 | 151 | 140 | 6.00 | 6.75 | 6.00 | 6.75 |
| 225 | 6.75 | 226 | 203 | 191 | 180 | 169 | 158 | 146 | 6.00 | 6.75 | 6.75 | 7.50 |
| 235 | 6.75 | 233 | 212 | 200 | 188 | 176 | 165 | 153 | 6.75 | 7.50 | 6.75 | 7.50 |
| 245 | 7.50 | 248 | 221 | 208 | 196 | 184 | 172 | 159 | 6.75 | 7.50 | 7.50 | 8.25 |
| 255 | 7.50 | 255 | 230 | 217 | 204 | 191 | 179 | 166 | 6.75 | 8.25 | 7.50 | 8.25 |
| 265 | 7.50 | 262 | 239 | 225 | 212 | 199 | 186 | 172 | 7.50 | 8.25 | 7.50 | 8.25 |
| 275 | 8.25 | 276 | 248 | 234 | 220 | 206 | 193 | 179 | 7.50 | 9.00 | 8.25 | 9.00 |
| 285 | 8.25 | 283 | 257 | 242 | 228 | 214 | 200 | 185 | 7.50 | 9.00 | 8.25 | 9.00 |
| 295 | 9.00 | 298 | 266 | 251 | 236 | 221 | 207 | 192 | 8.25 | 9.00 | 9.00 | 9.75 |
| 305 | 9.00 | 305 | 275 | 259 | 244 | 229 | 214 | 198 | 8.25 | 9.75 | 9.00 | 9.75 |
| 315 | 9.00 | 312 | 284 | 268 | 252 | 236 | 221 | 205 | 9.00 | 9.75 | 9.00 | 10.50 |
| 325 | 9.75 | 327 | 293 | 276 | 260 | 244 | 228 | 211 | 9.00 | 10.50 | 9.75 | 10.50 |
| 335 | 9.75 | 334 | 302 | 285 | 268 | 251 | 235 | 218 | 9.00 | 10.50 | 9.75 | 10.50 |
| 345 | 10.50 | 348 | 311 | 293 | 276 | 259 | 242 | 224 | 9.75 | 10.50 | 10.50 | 11.75 |
| 355 | 10.50 | 355 | 320 | 302 | 284 | 266 | 249 | 231 | 9.75 | 11.75 | 10.50 | 11.75 |
| 365 | 10.50 | 362 | 329 | 310 | 292 | 274 | 256 | 237 | 9.75 | 11.75 | 10.50 | 11.75 |
| 375 | 10.50 | 369 | 338 | 319 | 300 | 281 | 263 | 244 | 10.50 | 11.75 | 10.50 | 12.25 |
| 385 | 11.75 | 389 | 347 | 327 | 308 | 289 | 270 | 250 | 10.50 | 12.25 | 11.75 | 12.25 |
| 395 | 11.75 | 396 | 356 | 336 | 316 | 296 | 277 | 257 | 10.50 | 12.25 | 11.75 | 13.00 |
| 405 | 11.75 | 403 | 365 | 344 | 324 | 304 | 284 | 263 | 11.75 | 13.00 | 11.75 | 13.00 |
| 415 | 12.25 | 415 | 374 | 353 | 332 | 311 | 291 | 270 | 11.75 | 13.00 | 12.25 | 13.00 |
| 425 | 12.25 | 422 | 383 | 361 | 340 | 319 | 298 | 276 | 11.75 | 13.00 | 12.25 | 14.00 |
| 435 | 13.00 | 437 | 392 | 370 | 348 | 326 | 305 | 283 | 11.75 | 14.00 | 13.00 | 14.00 |
| 445 | 13.00 | 444 | 401 | 378 | 356 | 334 | 312 | 289 | 12.25 | 14.00 | 13.00 | 14.00 |
| 455 | 13.00 | 451 | 410 | 387 | 364 | 341 | 319 | 296 | 12.25 | 14.00 | 13.00 | 15.00 |
| Footnotes a to d: see next page. |

a

For a given series, follow either "option 1" or "option 2" as a guideline for the nominal tyre section, SN:

Option 1	Option 2

...	...

175	175

185	185

195	195

205	205

215	215

225	225

235	235

255	245

275	265

295	285

315	305

Continue	Continue

with either "option a"	with either "option b" or "option b"	or "option c"

b

c d

These lists are open-ended. For other nominal tyre section widths, SN, other annexes will be established as necessary. The figures are based on normal tread pattern tyres.

Other rims may be specified in relation to special services by agreement among tyre, rim, wheel and motor vehicle manufacturers

Not For Sale- PSQCA (c)

Only for Research Purpose

| Option a | Option b | Option c |
| --- | --- | --- |
| 345 | 335 | 325 |
| 375 | 365 | 355 |
| 405 | 395 | 385 |
| 435 | 425 | 415 |
| ... | 455 | 445 |
| ... | ... | ... |

Not For Sale- PSQCA (c)

Table B.2 — Dimensional guidelines for metric “60”, “55” and “50” series tyres on 15° drop-centre rims

| Nominal section width ab mm | Measuring rim width code K4 = 0,8 | Design section width mm | Design section height c, H mm | Approved rim width codes d |
| --- | --- | --- | --- | --- |
|  |  |  |  | min. | max. |
|  |  |  | Nominal aspect ratios, H/S | Nominal aspect ratios, H/S | Nominal aspect ratios, H/S |
|  |  |  | 60 | 55 | 50 | 60 | 55 | 50 | 60 to 55 | 50 |
| 175 | 5,25 | 172 | 105 | 96 |  | 5.25 | 5.25 |  | 6.00 |  |
| 185 | 6,00 | 187 | 111 | 102 |  | 5.25 | 6.00 |  | 6.00 |  |
| 195 | 6,00 | 194 | 117 | 107 |  | 6.00 | 6.00 |  | 6.00 |  |
| 205 | 6,75 | 208 | 123 | 113 |  | 6.00 | 6.00 |  | 6.75 |  |
| 215 | 6,75 | 215 | 129 | 118 |  | 6.00 | 6.75 |  | 6.75 |  |
| 225 | 6,75 | 222 | 135 | 124 |  | 6.75 | 6.75 |  | 7.50 |  |
| 235 | 7,50 | 236 | 141 | 129 |  | 6.75 | 7.50 |  | 7.50 |  |
| 245 | 7,50 | 243 | 147 | 135 |  | 7.50 | 7.50 |  | 8.25 |  |
| 255 | 8,25 | 257 | 153 | 140 |  | 7.50 | 7.50 |  | 8.25 |  |
| 265 | 8,25 | 264 | 159 | 146 |  | 7.50 | 8.25 |  | 8.25 |  |
| 275 | 9,00 | 278 | 165 | 151 |  | 8.25 | 8.25 |  | 9.00 |  |
| 285 | 9,00 | 285 | 171 | 157 |  | 8.25 | 9.00 |  | 9.00 |  |
| 295 | 9,00 | 292 | 177 | 162 |  | 9.00 | 9.00 |  | 9.75 |  |
| 305 | 9,75 | 306 | 183 | 168 |  | 9.00 | 9.00 |  | 9.75 |  |
| 315 | 9,75 | 313 | 189 | 173 |  | 9.00 | 9.75 |  | 10.50 |  |
| 325 | 10,50 | 328 | 195 | 179 |  | 9.75 | 9.75 |  | 10.50 |  |
| 335 | 10,50 | 334 | 201 | 184 |  | 9.75 | 10.50 |  | 10.50 |  |
| 345 | 10,50 | 341 | 207 | 190 | 173 | 10.50 | 10.50 | 10.50 | 11.75 | 11.75 |
| 355 | 11,75 | 361 | 213 | 195 | 178 | 10.50 | 10.50 | 11.75 | 11.75 | 11.75 |
| 365 | 11,75 | 368 | 219 | 201 | 183 | 10.50 | 11.75 | 11.75 | 11.75 | 12.25 |
| 375 | 11,75 | 374 | 225 | 206 | 188 | 10.50 | 11.75 | 11.75 | 12.25 | 12.25 |
| 385 | 12,25 | 386 | 231 | 212 | 193 | 11.75 | 11.75 | 12.25 | 12.25 | 13.00 |
| 395 | 12,25 | 393 | 237 | 217 | 198 | 11.75 | 12.25 | 12.25 | 13.00 | 13.00 |
| 405 | 13,00 | 407 | 243 | 223 | 203 | 11.75 | 12.25 | 13.00 | 13.00 | 14.00 |
| 415 | 13,00 | 414 | 249 | 228 | 208 | 12.25 | 13.00 | 13.00 | 13.00 | 14.00 |
| 425 | 13,00 | 421 | 255 | 234 | 213 | 12.25 | 13.00 | 13.00 | 14.00 | 14.00 |
| 435 | 14,00 | 438 | 261 | 239 | 218 | 13.00 | 13.00 | 14.00 | 14.00 | 15.00 |
| 445 | 14,00 | 445 | 267 | 245 | 223 | 13.00 | 14.00 | 14.00 | 14.00 | 15.00 |
| 455 | 15,00 | 462 | 273 | 250 | 228 | 13.00 | 14.00 | 14.00 | 15.00 | 15.00 |
| 465 | 15,00 | 469 |  |  | 233 |  |  | 15.00 |  | 16.00 |
| 475 | 15,00 | 475 |  |  | 238 |  |  | 15.00 |  | 16.00 |
| 485 | 16,00 | 492 |  |  | 243 |  |  | 15.00 |  | 16.00 |
| 495 | 16,00 | 499 |  |  | 248 |  |  | 16.00 |  | 17.00 |
| 505 | 16,00 | 506 |  |  | 253 |  |  | 16.00 |  | 17.00 |
| Footnotes a to d: see Table B.1 |

Only for Research Purpose

Not For Sale- PSQCA (c)

Table B.3 — Dimensional guidelines for metric series “45” series tyres on 15° drop centre rims

| Nominal section width ab SN mm | Measuring rim width code Rm K4 = 0,85 | Design section width S mm | Design section height c H mm | Approved rim width code d |
| --- | --- | --- | --- | --- |
|  |  |  |  | min. | max. |
| 355 | 11.75 | 354 | 160 | 11.75 | 11.75 |
| 365 | 12.25 | 365 | 164 | 11.75 | 12.25 |
| 375 | 12.25 | 372 | 169 | 11.75 | 12.25 |
| 385 | 13.00 | 386 | 173 | 12.25 | 13.00 |
| 395 | 13.00 | 393 | 178 | 12.25 | 13.00 |
| 405 | 14.00 | 410 | 182 | 13.00 | 14.00 |
| 415 | 14.00 | 416 | 187 | 13.00 | 14.00 |
| 425 | 14.00 | 423 | 191 | 13.00 | 14.00 |
| 435 | 15.00 | 440 | 196 | 14.00 | 15.00 |
| 445 | 15.00 | 446 | 200 | 14.00 | 15.00 |
| 455 | 15.00 | 453 | 205 | 14.00 | 15.00 |
| 465 | 16.00 | 469 | 209 | 15.00 | 16.00 |
| 475 | 16.00 | 476 | 214 | 15.00 | 16.00 |
| 485 | 16.00 | 483 | 218 | 15.00 | 16.00 |
| 495 | 17.00 | 499 | 223 | 16.00 | 17.00 |
| 505 | 17.00 | 506 | 227 | 16.00 | 17.00 |
| 515 | 17.00 | 513 | 232 | 16.00 | 17.00 |
| 525 | 18.00 | 529 | 236 | 17.00 | 18.00 |
| Footnotes a to d: see Table B.1 |

Only for Research Purpose

Annex C

(informative)

Tyre dimension tables

Example of dimension table of a tyre having nominal section width 185, nominal aspect ratio 90, radial, nominal rim diameter code 16, mounted on 5° tapered rim:

| Tyre size designation | Measuring rim width code | Design tyre | Maximum tyre dimensions in-service |
| --- | --- | --- | --- |
|  |  | Section width S mm | Overall diameter Do mm | Overall width Wmax mm | Overall diameter Do,max mm |
| 185/90 R 16 | 5.00 | 184 | 740 | 193 | 753 |

Not For Sale- PSQCA (c)

Example of dimension table of a tyre having nominal section width 265, nominal aspect ratio 75, diagonal, nominal rim diameter code 19.5, mounted on 15° tapered rim (drop-centre):

| Tyre size designation | Measuring rim width code | Design tyre | Maximum tyre dimensions in-service |
| --- | --- | --- | --- |
|  |  | Section width S mm | Overall diameter Do mm | Overall width Wmax mm | Overall diameter Do,max mm |
| 265/75 D 19.5 | 7.50 | 262 | 893 | 280 | 925 |

Example of dimension table of a tyre having nominal section width 305, nominal aspect ratio 45, construction Z, nominal rim diameter 500, mounted on a new concept rim with a rim/section ratio 0,5:

| Tyre size designation | Measuring rim width mm | Design tyre | Maximum tyre dimensions in-service |
| --- | --- | --- | --- |
|  |  | Section width S mm | Overall diameter Do mm | Overall width Wmax mm | Overall diameter Do,max mm |
| 305/45 Z 500 | 150 | 304 | 814 | 314 | 824 |