(ICS No: 67.200.10)

PAKISTAN STANDARD

FOR

PALM OIL OIL EDIBLE GRADE

(1ST REVISION)

(ALL RIGHTS RESERVED)

PAKISTAN STANDARDS AND QUALITY CONTROL AUTHORITY

Standards Development Centre,

39 – Garden Road, Saddar,

Karachi-74400

TABLE – 1

REQUIREMENTS FOR PALM OIL EDIBLE GRADE

(Clause 3.4)

| SL. NO. | CHARACTERISTICS | REQUIREMENTS |
| --- | --- | --- |
| (1) | (2) | (3) |
| i. | Moisture and insoluble impurities, % by wt. max. | 0.1 |
| ii. | Colour in a 1-inch cell on lovibond scale express as (Y + 10 R), max. | 60 |
| iii. | Refractive index *at 50 0C. | 1.4491 to 1.4552 |
| iv. | Saponification value | 195 to 205 |
| v. | Iodine value (wijs). | 50 to 55 |
| vi. | Free fatty acids (as oleic acid) % by wt. | 0.25 |
| vii. | Unsaponifiable matter, % by weight, max. | 1.2 |
| viii. | Melting point, 0C, (Open capillary slip method). | 36 ± 2 |
| ix. | Peroxide value, expressed as milliequivalents oxygen per kg, max. | 10 |
| x. | Rancidity (Kries Test) **. | 3.0 R |
| xi. | Vitamin – A, | 33000 I.U. to 45000 I.U per kg, of finished product |
| xii. | Vitamin-D3, | 3000 I.U. to 4500 I.U per kg, of finished product |

NOTE:	Vitamin A & D3 in Bulk Oils on Import Stage is not necessary.

TABLE-2

REQUIREMENTS FOR CONTAMINANTS

|  | Contaminant Limits |
| --- | --- |
| Matter volatile at 105°C | Not more than 0.2% |
| Insoluble impurities | Not more than 0.05% m/m |
| Iron (Fe) | Not more than 1.5 mg/kg |
| Copper (Cu) | Not more than 0.1 mg/kg |
| Lead (Pb) | Not more than 0.1 mg/kg |
| Arsenic (As) | Not more than 0.1 mg/kg |