(ICS No: 67.200.20)

PAKISTAN STANDARD

FOR

REFINED MAIZE CORN OIL

(1ST REVISION)

_____________________________________________________________________________________________

(ALL RIGHTS RESERVED)

PAKISTAN STANDARDS AND QUALITY CONTROL AUTHORITY

Standards Development Centre,

39 – Garden Road, Saddar,

Karachi-7440

## TABLE – 1

# REQUIREMENTS FOR REFINED MAIZE (CORN) OIL

| SL.NO. | CHARACTERISTIC | LIMITS | REF.TO CLAUSE OF PS: 56-1996* |
| --- | --- | --- | --- |
| i. | Moisture, percent by weight, Max. | 0.1 | 4 & 5 |
| ii. | Colour in a 5 ¼ inch cell on lovibond scale, max. | R - 5 Y - 50 | 12 |
| iii. | Refractive index* at 40 0C. | 1.4645 to 1.4675 | 9 |
| iv. | Saponification value. | 187 to 195 | 14 |
| v. | Iodine value (Wijs). | 103 to 130 | 13 |
| vi. | Free Fatty Acid (as oleic acid) percent by weight, max. | 0.25 | 6 |
| vii. | Unsaponifiable matter, percent by weight, max. | 1.5 | 7 |
| viii. | Peroxide value, expressed as milliequivalents oxygen per kg, Max. | 10 | 20 |
| ix. | Anisidine Value max / Rancidity (Kries Test), max. *** | 3.0 R | See Appendix-C of PS:221-2003 (3rd Rev.)** |
| x. | Vitamin-A | 33000 I.U. to 45000 I.U. per kg of the finished product. | 23 |
| xi. | Vitamin-D3 | 3000 I.U. to 4500 I.U. per kg of the finished product. |  |
| xii. | Soap content., ppm, max. | 50 | Appendix-D of PS:221-2003 (3rd Rev.)** |

NOTE:	Vitamin A & D3 in Bulk Oils on Import Stage is not necessary.

TABLE-2

REQUIREMENTS FOR CONTAMINANTS

|  | Contaminant Limits |
| --- | --- |
| Matter volatile at 105°C | Not more than 0.2% |
| Insoluble impurities | Not more than 0.05% m/m |
| Iron (Fe) | Not more than 1.5 mg/kg |
| Copper (Cu) | Not more than 0.1 mg/kg |
| Lead (Pb) | Not more than 0.1 mg/kg |
| Arsenic (As) | Not more than 0.1 mg/kg |