ICS No.67.200.20

PAKISTAN STANDARD SPECIFICATION

FOR

REFINED PALM OLEIN (1ST REV.).

(ALL RIGHTS RESERVED)

PAKISTAN STANDARDS AND QUALITY CONTROL AUTHORITY

Standards Development Centre,

39 – Garden Road, Saddar,

Karachi-7440

## TABLE – 1

# REQUIREMENTS FOR REFINED PALM OLEIN

(CLAUSE 3.5)

| SL. NO | CHARACTERISTIC | LIMITS | REF.TO CLAUSE OF PS: 56-1996* |
| --- | --- | --- | --- |
| i. | Moisture percent by weight, Max. | 0.1 | 4 |
| ii. | Insoluble Impurities percent by weight, Max. | 0.05 | 4 |
| iii. | Matter volatile at 105°C | Not more than 0.2% | - |
| iv. | Colour in a 5 ¼ inch cell on lovibond scale max. | R - 5 Y - 50 | 12 |
| v. | Refractive index* at 40 0C. | 1.4550 to 1.4610 | 9 |
| vi. | Saponification value. | 195 to 205 | 14 |
| vii. | Iodine value (Wijs). | 56 to 64 | 13 |
| viii. | Free Fatty Acid (as palmitic acid) percent by weight, max. | 0.25 | 6 |
| ix. | Unsaponifiable matter, percent by weight, max. | 1.2 | 7 |
| x. | Peroxide value, expressed as milliequivalents oxygen per kg, Max. | 10 | 20 |
| xi. | Anisidine Value max / Rancidity (Kries Test) max***. | 3.0 R | See App.-C of PS: 221-2003(3rd Rev.) for Anisidine Value or See App. A of PS:2858-2003 (R) for Rancidity Test |
| xii. | Vitamin-A | 33000 I.U. to 45000 I.U per kg of the finished product. | 23 |
| xiii. | Vitamin-D3 | 3000 I.U. to 4500 I.U. per kg of the finished product. | - |
| xiv | Slip melting point., max. | 24 0C | 8 |
| xv | Cloud point 0C, Max. | 10 0C | PS:ISO:3015-1992** |
| xvi | Soap content, ppm, max. | 50 | Appendix-D of PS:221-2003 (3rd Rev.)**** |
| xvii | Iron (Fe) | Not more than 1.5 mg/kg | - |
| xviii | Copper (Cu) | Not more than 0.1 mg/kg | - |
| xix | Lead (Pb) | Not more than 0.1 mg/kg | - |
| xx | Arsenic (As) | Not more than 0.1 mg/kg | - |