ICS No.67.100.200

PAKISTAN STANDARD

FOR

MARGARINE (3RD REVISION)

(ALL RIGHTS RESERVED)

PAKISTAN STANDARDS AND QUALITY CONTROL AUTHORITY,

STANDARDS DEVELOPMENT CENTRE,

PSQCA Complex, Standardization Wing-II, Plot No. ST.7/A, Block-3,

Scheme-36, Gulistan-e-Jouhar,

Karachi-Pakistan

Table 2

| Requirements for Margarine |
| --- |
|  | Characteristics | Requirements |
| 1 | Moisture percent by wt. max | 16 |
| 2 | Oil/Fat percent by wt. min. | 80 |
| 3 | Free Fatty acid (as Oleic acid) of the constituent Oil/Fat, percent by wt. max | 0.35 |
| 4 | Unsaponifiable matter of the constituent Oil/Fat, percent by wt., max | 1.5 |
| 5 | Peroxide value expressed as milliequivalent oxygen per Kg. max | For Table Margarine: 10 For Industrial Margarine: 5 |
| 6 | Slip Melting Point maximum | For Table Margarine: 38.5 °C For Industrial Margarine: 48°C |
| 7 | Metal Contaminants , Parts per million , max |
|  | Iron (Fe) | 1.5 |
|  | Copper (Cu)/Lead (Pb)/Arsenic(As) | 0.1 |
|  | Nickel (Ni) | 0.5 |
| 8 | Vitamin 'A' I.U per Kg. of finished product, min. | 33,000 +10% |
| 9 | Other Vitamins | Limited by GMP |

Table 3

| Requirements for Margarine Spreads |
| --- |
|  | Characteristics | Requirements |
| 1 | Moisture percent by wt. | 39 |
| 2 | Oil/Fat percent by wt. min | <60 and > 40 |
| 3 | Free Fatty acid (as Oleic acid) of the constituent Oil/Fat, percent by wt. max | 0.35 |
| 4 | Unsaponifiable matter of the constituent Oil/Fat, percent by wt., max | 1.5 |
| 5 | Peroxide value expressed as milliequivalent oxygen per Kg. max | 10 |
| 6 | Slip Melting Point maximum | For water continuous: Not Applicable For Oil continuous 42°C |
| 7 | Metal Contaminants , Parts per million , max |
|  | Iron (Fe) | 1.5 |
|  | Copper (Cu)/Lead (Pb)/Arsenic(As) | 0.1 |
|  | Nickel (Ni) | 0.5 |
| 8 | Vitamin-‘A’ I.U. per kg of finished product. | 33,000 to 4500 |
| 9 | Vitamin D3 I.U. per kg of finished product. | 3000 to 4500 |
| 10 | Other Vitamins | Limited by GMP |

5.	SHELF LIFE:

“shelf life of Margarine, Margarine Spread and Spread shall not be more than 9 months and for Industrial Margarine not more than 12 months.

6.	MICROBIOLOGICAL REQUIREMENTS:

Margarine and Margarine Spreads shall comply with the microbiological requirements given in Table-4.

TABLE- 4

| Microorganisms | Limits |
| --- | --- |
| Total Viable Plate Count | < 25000 cfu/g |
| Coliforms | < 100 cfu/g |
| Yeast and Mould | < 1000 cfu/g |
| Salmonella | Negative in 25 ml or g |
| Listeria | Negative in 25 ml or g |
| Staph. Aureus | Negative in 25 ml or g |