ICS No: 67.160.20:13.060.10

PAKISTAN STANDARD SPECIFICTION

FOR

BOTTLED NATURAL MINERAL WATERS

(3RD REVISION)

(ALL RIGHTS RESERVED)

PAKISTAN STANDARDS AND QUALITY CONTROL AUTHORITY

Standards Development Centre,

PSQCA Complex, Standardization Wing II, 1st Floor, Plot - ST-7/A, Block-3, Scheme No.36, Gulistan-e-Jauher, Karachi

TABLE–I

PHYSICAL & CHEMICAL REQUIREMENTS

| SL. NO. | PARAMETERS | LIMITS |
| --- | --- | --- |
| 1. | pH Range. | 6.5 – 8.5 |
| 2. | Total dissolved solids (TDS), max. | 1000 mg/L |
| 3. | Total hardness as CaCo3 ,max | 250 mg/L |
| 4. | Nitrite (NO2) | 0.020 mg/L |
| 5. | Chloride max. | 250 mg/L |
| 6. | Sulphate max. | 100 mg/L |
| 7. | Sodium max. | 30 mg/L |
| 8. | Potassium max. | 30 mg/L |
| 9. | Magnesium max. | 100 mg/L |
| 10. | Calcium max. | 200 mg/L |

TABLE–II

CHARACTERISTIC MAXIMUM ADDMISSIBLE CONCENTRATION (mg/L)

| Parameters | Limits |
| --- | --- |
| Antimony (Sb) | 0.005 |
| Arsenic (As) | 0.01 |
| Barium (Ba) | 0.71 |
| Borate (B) | 1.5 |
| Cadmium (Cd) | 0.003 |
| Chromium (Cr) | 0.05 |
| Copper (Cu) | 1.0 |
| Cyanide (CN) | 0.070 |
| Fluoride (F) | As per Codex section 7.3.2 of CXS 108-1981 |
| Lead (Pb) | 0.01 |
| Manganese (Mn) | 0.4 |
| Mercury (Hg) | 0.001 |
| Nickel (Ni) | 0.02 |
| Nitrate (NO3) | 50, Calculated as nitrate |
| Nitrite | 0.1 as nitrate |
| Selenium (Se) | 0.01 |
| Boron (B) | 2.4 |

TABLE–III

MICROBIOLOGICAL LIMITS

| Sl. # | Organisms | Recommended Value |
| --- | --- | --- |
| 1 | Total coliform | < 1 CFU / 250 ml |
| 2 | Thermotolerant / Fecal coliform | < 1 CFU / 250 ml |
| 3 | E-coli | < 1 CFU / 250 ml |
| 4 | Fecal enterococci/streptococci | < 1 CFU / 250 ml |
| 5 | Pseudomonas aeruginosa | < 1 CFU / 250 ml |
| 6 | Total viable count at 20 – 22 oC | < 100 CFU / ml |
| 7 | Total viable count at 37 oC | < 20 CFU / ml |

# Text boxes

Optional